### SPECIFICATIONS FOR

TENDER # 1271-1021

EXTERIOR RENOVATIONS

Corner Brook Interfaith Home Cottages #1

Units 1-44, Churchill Crescent

CLOSING DATE:	27 April 2010

CLOSING TIME:		11:00 AM (Newfoundland Time)

Invitation to Tender for  Exterior Renovations Corner Brook Interfaith Cottages

- General Provisions

  - Intent

This invitation to Tender is intended to request bids for the Exterior Renovations to the Corner Brook Interfaith Cottages, units # 1-44, for the Western Regional Health Authority (Western Health).

  - Client Background

Western Health was established in 2005 and is responsible for the delivery of Health and Community Services in the Western Region.

  - Vendor Response

1.3.1	Vendor’s tender must contain an Executive Summary which shall contain:

- A brief description of the project/services  being quoted.

- The name, title and address of the Vendor’s representative responsible for the preparation of the Tender.

    - All prices quoted for goods and services must be specified in Canadian dollars, FOB .  All Tenders will be held to be valid for ninety (90) days following the Tender closing date.

    - Tenders must be received in full on or before the exact closing time and date indicated.  TENDERS RECEIVED AFTER THAT TIME WILL NOT BE CONSIDERED.

1.3.4	All costs relating to the work and materials supplied by the Vendor in responding to this Invitation to Tender must be borne by the Vendor.

1.4	Release of Information

    - While Tender is Open:

The names of individuals or companies who have picked up the tender documents will not be released.

1.4.2	At Tender Opening:

Only the names of the bidders will be read out.

1.4.3	After Tender Opening:

1.	No further information will be released until after the contract is awarded.

2.	After award, only the name and bid price of the successful bidder will be made available.

3.	Information will be made available for a 90 day period only.

4.	Successful Awards will be posted on Web Site.

1.4.4	FYI, Statements that are included as part of our Tender calls:

While bidders are welcome to attend the public opening, please be advised that it is not our policy to release bid information.  Only the names of the bidders will be released.

1.5	Communication During Tendering

1.5.1	All communications with Western Health with respect to this invitation to Tender must be directed in writing to the attention of:

Mr. John Piercey

Regional Director, Materiels Management

Western Health

P.O. Box 2005

Corner Brook, Newfoundland

A2H 6J7

Tel:  (709) 637-5511

Fax:  (709) 634-2649

Email:  johnpiercey@westernhealth.nl.ca

1.5.2	Western Health may, during the assessment period, request meetings with the Vendors to clarify points in the Tender.  No changes by the Vendor will be permitted after the Tender closing date.

1.5.3	Faxed Tender responses will be accepted with the condition that the original Tender documents are received at Western Health’s Materials Management Department no later than Five working days following the Tender closing date.

1.5.4	All bids must be sent in a sealed envelope clearly marked with Tender Name and Number to:	Materials Management Department, Western Health, Western Memorial Regional Hospital, Lower Level, P.O. Box 2005, Corner Brook, NL  A2H 6J7.

    - Bids submitted by electronic transmission (e-mail) will not be accepted.

    - Companies submitting fax Tenders are doing so at their own risk and the fax Tender must be at the public opening as specified in the Tender information.  This Authority will not be responsible for in-house courier services if companies submit quotations by fax machine.  The time stated on the fax Tender will become null and void since it is the responsibility of the company placing the Tender to have their Tender at the public opening, therefore, this Authority will not be responsible for any damages or liabilities.

    - In order to contribute to waste reduction and promote environmental protection, the Western Health will endeavour to acquire goods and services that support these principles, therefore, product(s) quoted should include:

- maximum level of post-consumer waste and/or recyclable content

- minimal packaging

- minimal environmental hazards

- maximum energy efficiency

- potential for recycling

- disposal costs

- must not reduce the quality of the product required or affect the intended use of the product

- must not significantly impact the acquisition cost

    - Are the quoted price(s) on this tender (where applicable) available to our employees?

Yes	      	No 	       N/A

Administratively the Western Integrated Health Authority will not be involved in ordering, servicing, warranty and payment; the employee(s) would deal directly with the company.

1.6	Tender Acceptance

1.6.1	Any acquisitions resultant from this invitation to Tender shall be subject to the Public Tendering Act.

    - The Tenders shall be opened in the Private Dining Room at The Western Memorial Regional Hospital on the scheduled date and time.

    - Any Tender may be accepted in whole or in part.  The lowest Tender may not necessarily be accepted and Western Health reserves the right to cancel the Tender call.  Western Health shall not be held responsible or liable for the payment of any costs that are incurred by the bidder in preparing a Tender in response to this invitation to Tender.

1.7	Warranty

1.7.1	The Vendor shall warrant that the product and services supplied to Western Health shall equal the published specifications.

    - The Vendor shall provide no less than a 1-year warranty on the system.  The Vendor agrees to provide free of charge all parts and labour necessary to repair the system during the first year of operation.

    - Vendor shall indicate the warranty start date ________________.

    - Vendor shall indicate the individual who will be providing the service and the nearest service location.

______________________		_____________________

    - Is a board replacement program available and at what cost?

Yes        No

Cost: _____________

- Project Specifications

1. Summary of Work

The Corner Brook Interfaith Home Cottages #1 development consists of 44 single bedroom rental units in 22 duplexes built in 1974.

Work of this contract comprises:

1. The removal and proper disposal of all roofing materials, soffit, fascia, siding, windows, and exteriors doors.

2. The installation of ice and water shield, asphalt shingles, 25mm insulation, vinyl siding c/w trims, vinyl windows and exterior storm doors and exterior steel doors.

Shop drawings are to be submitted prior to ordering of materials.  Allow 10 days for Western Health to review.

2. Waste Management and Disposal

Any materials which can be recycled are to be collected, separated and stored on site until such time they are transported to a recycling facility.

Any windows and doors deemed salvageable by Western Health will be identified prior to commencement of work and are to be carefully removed and stored on site to allow collection by Western Health.

All waste material is to be removed from site in a timely manner and disposed of in accordance with local regulations.

Deconstruction of the exteriors will be limited to a maximum of 3 duplexes at any one time.

3. Asphalt Shingles

3.1 Removal of Existing Roofing

Remove existing roofing, flashings and underlay, and expose sheathing or shingle lath of roof.  Withdraw existing shingle and flashing nails and set those which break off.  Leave surfaces free of dirt and loose material.  A Western Health Representative will inspect sheathing prior to installation of any materials.  Take up, cut out, portion of sheathing boards affected by fungal or insect attack as directed by Western Health Representative.

## 3.2 Materials

### Asphalt shingles: to CSA A123.1/A123.5.

#### Type: self-seal, standard, pattern rectangular

#### Mass: minimum 33 kg/3m²

#### Colours:  as selected by Owner’s Representative

### Roofing underlayment: self-adhesive, non-woven glass fibre matt coated

### with SBS modified bitumen, minimum thickness 1.8 mm, bottom surface

### release film, top surface sanded.  To be applied to entire roof surface.

### Continuous Ridge Vent: minimum 285 mm wide durable, copolymer plastic

### ridge vent, providing minimum 357 cm2/m net free vent area, capable of

### accepting asphalt shingle cap over for shingle finish.

### Cement: Plastic cement: to CAN/CGSB-37.5.

### Nails: to CSA B111, of galvanized steel, sufficient length to penetrate 19

### mm into deck.

## 3.3 Application

### 1. 	Do asphalt shingle work in accordance with CAN3-A123.51/CAN3-A123.52, NBC/CRCA Specification, except where specified otherwise.

### 2. 	Install layer of self-adhesive roof underlayment over the entire roof area.

### 3.	 Install drip edge along eaves, overhanging 12 mm, with minimum 50 mm flange extending onto roof decking. Nail to deck at 400 mm oc.

### 4. 	Install bottom step flashing (soaker base flashing) interleafed between shingles at vertical junctions.

### 5. 	Install asphalt shingles on roof slopes 1:3 and steeper in accordance with CAN3-A123.51 supplemented as follows:

### 6. 	Install asphalt shingles on roof slopes 1:6 to less than 1:3 in accordance with CAN3-A123.52 supplemented as follows.

## 3.4 Prefinished Sheet Metal and Trim

### 1. 	Prefinished sheet with factory applied polyvinylidene fluoride.

### 2. 	Class F1S

#### 3. 	Colour as selected by Owner’s Representative from manufacturer's standard range.

#### 4. 	Specular gloss: 30 units +/- 5 in accordance with ASTM D523.

#### 5. 	Coating thickness: not less than 22 micrometres.

#### 6. 	Resistance to accelerated weathering for caulk rating of 8, colour fade 5 units or less and erosion rate less than 20 % to ASTM D822 as follows:

##### 1.Outdoor exposure period 2500 hours.

##### 2.    Humidity resistance exposure period 5000 hours.

### 3.5. Board Insulation

### Expanded polystyrene (EPS): for use below grade and exterior walls:  to CAN/ULC-S701 Type 2, shiplapped edges, RSI 0.70 per 25 mm, total thickness of 25mm.

### 5. Plastic Siding

### 5.1 Submittals

### 1. Product Data: Submit manufacturer's printed product literature, specifications and data sheet.

### a. Submit two copies of WHMIS MSDS - Material Safety Data Sheets. Indicate VOC's for caulking materials during application and curing.

### 2.    Submit duplicate 300 x 300 mm samples of siding material, of color and profile specified.

### Shop drawings to indicate dimensions, siding profiles, attachment methods, schedule of wall elevations, trim and closure pieces, soffits, fascia, and related work.

### Submit manufacturer’s installation instructions.

5.2 Warranty

Provide a written guarantee, signed and issued in the name of the owner, covering the plastic cladding/siding for both material and workmanship for a period of 10 (ten) years from the date of Substantial Completion.

5.3 Materials

1. Rigid vinyl: extruded polyvinylchloride to CAN/CGSB-41.24 wood grain or embossed finish, vertical bevel profile, 2 x 100 mm wide x maximum permissible length, min thickness 0.042”, of color selected by Owner’s Representative.  Standard of acceptance: Royal Building Products “Colorscapes” or approved equal.

2. Accessories: internal corners, external corners (125mm width), cap strip, drip cap, undersill trim, starter strip and window/door trim of extruded plastic, same material and color as siding, with nailing strip pre-punched.

3. Exterior wall sheathing membrane: to CAN/CGSB-51.32 spunbonded olefin type as indicated.

4. Fasteners: nails to CSA B111, screws to ANSI B18.6.4 aluminum purpose made.

5. Galvanized steel sheet: commercial grade to ASTM A652M with Z275 zinc coating.

6. Aluminum sheet: mill finish plain utility sheet, 0.80 mm thick.

5.4 Installation

1. Install one layer sheathing membrane horizontally by nailing lapping edges 75 mm.

2. Install metal sill as indicated.

3. Install window/door opening flashings, starter strips, inside corners, edgings, drip and cap.

4. Install siding sequentially from starter strip up, in accordance with manufacturer/fabricators written instructions.

5. Install exterior corners, fillers and closure strips with carefully formed and profiled work.

6. Maintain joints in exterior panels, true to line, tight fitting, hairline joints.

7. Seal junctions with dissimilar materials with sealant. Do work in accordance with Section 07 92 00 - Joint Sealants.

8. Attach components in manner not restricting thermal movement. Conceal fasteners where possible.

### 6. Vinyl Windows

## 6.1 References

### 1. Canadian General Standards Board (CGSB)

#### 1. CAN/CGSB-79.1, Insect Screens.

### 2. Canadian Standards Association (CSA)

#### 1. CSA-A440-00/A440.1, A440, Windows / Special Publication A440.1, User Selection Guide to CSA Standard A440, Windows.

#### 2. CAN/CSA-Z91, Safety Code for Window Cleaning Operations.

#### 6.2 Submittals

### 1. Indicate materials and details in scale full size for head, jamb and sill, profiles of components, interior and exterior trim. Junction between combination units, elevations of unit, anchorage details, location of isolation coating, description of related components and exposed finishes fasteners, and caulking. Indicate location of manufacturer’s nameplates.

### 2. Shop drawings to include continuation of air barrier and vapour barrier between wall assembly and vinyl window.

### 3. Submit one complete full size window sample of each type window.

### 4. Include frame, sash, sill, glazing and weatherproofing method, insect screens, surface finish and hardware. Show location of manufacturer’s nameplates.

### 5. Include 150 mm long samples of head, jamb, sill, meeting rail, mullions to indicate profile.

## 6.3 Test Reports

### 1. Submit test reports from approved independent testing laboratories, certifying compliance with specifications, for:

#### Windows classifications

#### Air tightness

#### Water tightness

#### Wind load resistance

#### Condensation resistance

#### Forced entry resistance

#### Insect screens

#### Glazing

#### Safety drop – vertical sliding windows only

#### Ease of operation – windows with operable lights

#### Sash pull-off – vinyl windows

## 6.4 Warranty

### 1. Provide a written warranty for work under this Section from Manufacturer for failure due to defective materials and from Contractor for failure due to defective installation, workmanship for ten (10) years respectively.

## 6.5 Closeout Submittals

### 1. Provide operation and maintenance data for windows for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

## 6.6 Materials

### 1. Materials: to CSA-A440/A440.1 supplemented as follows:

### 2. All vinyl windows by same manufacturer.

### 3. Sash: vinyl.

### 4. Main frame: vinyl, thermally broken.

### 5. Glass: in accordance with Section 08 80 50 - Glazing.

### 6. Screens: to CAN/CGSB-79.1.

#### Insect screening mesh: count 18 x 14

#### Fasteners: tamper proof

#### Screen frames: aluminum, colour to match window frames

#### Mount screen frames for exterior replacement.

#### Provide full insect screens to cover entire window

## 6.7 Window Type and Classification

### 1. Types:

#### Casement with insulating glass.

#### Screens: screens as indicated.

### 2. Classification rating: to CSA-A440/A440.1 for various regions of Newfoundland and Labrador as follows:

#### Corner Brook	A3, B5, C4, I40, F1, S1, G1

### 3. Energy ratings: windows to be Energy Star certified to Canadian Standards Association for various regions of Newfoundland and Labrador as follows:

#### Island Region (excluding Northern Peninsula).

##### Zone B.

##### 6.8 Air Barrier and Vapor Retarder

### Provide low expanding, single component polyurethane foam sealant installed at head, jamb and sill perimeter of window for sealing to building air barrier, vapour retarder and window frame.  Foam sealant width to be adequate to provide required air tightness and            vapour diffusion control to building air barrier and vapour retarder foam interior.

### 6.9 Window Installation

### 1. Install in accordance with CSA-A440.

### 2. Arrange components to prevent abrupt variation in colour.

### 3. Install shims between windows and building frame at each installation screw location. Shim and fasten windows in accordance with manufacturer’s recommendations and CAN/CSA A440.4.

## 6.10 Caulking

### 1. Seal joints between windows and window sills with sealant. Caulk between sill upstand and window-frame. Caulk butt joints in continuous sills.

### 2.  Apply sealant in accordance with Section 07 92 00 - Joint Sealants. Conceal sealant within window units except where exposed use is permitted by owner’s representative.

7.   Exterior Doors

Both an aluminum storm door and exterior steel door are to be installed on each cottage meeting the following specifications.

Aluminum Storm Door (44 each)

Standard of acceptance is the AluminArt National 3-Lite.

Exterior Steel Door (44 each)

Standard of acceptance is the Atlantic Steel Entry System, Vinyl Clad (Prefinished White), 9-Lite.

8.   Exterior Light Fixtures

An exterior grade light fixture is required and is to be installed adjacent to each unit’s exterior door (44 in total).  Standard of acceptance is the Banvil2000 EW51-S Die Cast Aluminum fixture.

## TENDER CHECKLIST

TENDER #1271-1021

DID YOU INCLUDE

HAS TENDER SUBMISSION BEEN SIGNED					Yes 	    No

COPY OF REQUIRED TENDER DOCUMENTS    				Yes 	    No

COPY OF BROCHURES (IF REQUESTED)					Yes 	    No

COPY OF WCB LETTER OF GOOD STANDING (IF REQUIRED)		Yes 	    No

COPY OF PROOF OF INSURANCE (IF REQUIRED)				Yes 	    No

AMOUNT OF TAX NOTED ON REQUEST FOR QUOTATION FORM	Yes 	    No

OPTIONAL PRICING FOR TRAINING INCLUDED				Yes 	    No

NOTE:  	TENDER RESPONSES MAY BE REJECTED IF YOU ANSWER “NO” TO ANY OF THE ABOVE QUESTIONS.