### SPECIFICATIONS FOR

TENDER #0271-1626

SUPPLY OF cOMMERCIAL dISWASHER Washer

FOR WESTERN HEALTH

CLOSING DATE:	November 9th , 2016

CLOSING TIME:		2:00 PM (Newfoundland Time)

Invitation to Tender for Supply and installation of Dish Washer

- General Provisions

  - Intent

This invitation to tender is intended to obtain the supply of a Comercial Dishwasher for the  Bonne Bay Helth Centre in Norris Point, Newfoundland.  The successful vender will be responsible for the  supply of a dishwasher that meets all the requirements listed in the specifications section of as well as providing all neecessary training to staff for the use of the equipment. We are asking vendors to submit pricing for the equipment  and separate price for installation.  A decision will be made  regarding wether or not to include installation for this project  after prices are known.

Consideration for this tender will include the following:

- Ongoing service and maintenance support.

- All manuals, documents and initial supplies.

- The right to reproduce any printed materials supplied with the product for the purpose of using the product.

- Training and training manuals.

- Future enhancement availability.

- Products being fully suited, as determined by Western Health’s professional staff, for intended use and compatible with Western Health’s facilities and/or existing equipment.

  - Client Background

Western Health was established in 2005 by the Government of Newfoundland and is responsible for the delivery of Health and Community Services in the Western Newfoundland Region.

  - Vendor Response

1.3.1	Vendor’s tender must contain an Executive Summary which shall contain:

- A brief description of the product being quoted.

- The name, title and address of the Vendor’s representative responsible for the preparation of the Tender.

    - All prices quoted for goods and services must be specified in Canadian dollars, FOB Western Health.  All Tenders will be held to be valid for ninety (90) days following the Tender closing date.

    - Tenders must be received in full on or before the exact closing time and date indicated.  TENDERS RECEIVED AFTER THAT TIME WILL NOT BE CONSIDERED.

1.3.4	All costs relating to the work and materials supplied by the Vendor in responding to this Invitation to Tender must be borne by the Vendor.

1.4	Release of Information

    - While Tender is Open:

The names of individuals or companies who have picked up the tender documents will not be released.

1.4.2	At Tender Opening:

Only the names of the bidders  and the total price bid will be read out. No official award will be given until a detailed review of the bids is done to determine if all requirements are being met with a bid.

1.4.3	After Tender Opening:

1.	No further information will be released until after the contract is awarded.

2.	After award, only the name and bid price of the successful bidder will be made available.

3.	Information will be made available for a 90 day period only.

4.	Successful Awards will be posted on Web Site.

1.5	Communication during Tendering

1.5.1	All communications with Western Health with respect to this invitation to tender must be directed in writing to the attention of:

Mr. Paul Wight

Regional Director, Materials Management

Western Health

Corner Brook, Newfoundland

A2H 6J7

Tel:  (709) 637-5511

Fax:  (709) 634-2649

Email: paulwight@westernhealth.nl.ca

1.5.2	Western Health may, during the assessment period, request meetings with the Vendors to clarify points in the Tender Bid.  No changes by the Vendor will be permitted after the Tender closing date.

1.5.3	Faxed Tender responses will be accepted with the condition that the original Tender documents are received at Western Health’s Materials Management Department no later than Five working days following the Tender closing date.

1.5.4	All bids must be sent in a sealed envelope clearly marked with Tender Name and Number to:	Materials Management Department, Western Health, Western Memorial Regional Hospital, Lower Level, P.O. Box 2005, Corner Brook, NL  A2H 6J7.

    - Bids submitted by electronic transmission (e-mail) will not be accepted.

    - Companies submitting fax Tenders are doing so at their own risk and the fax Tender must be at the public opening as specified in the Tender information.  This Authority will not be responsible for in-house courier services if companies submit quotations by fax machine.  The time stated on the fax Tender will become null and void since it is the responsibility of the company placing the Tender to have their Tender at the public opening, therefore, this Authority will not be responsible for any damages or liabilities.

    - In order to contribute to waste reduction and promote environmental protection, the Western Health will endeavour to acquire goods and services that support these principles, therefore, product(s) quoted should include:

- maximum level of post-consumer waste and/or recyclable content

- minimal packaging

- minimal environmental hazards

- maximum energy efficiency

- potential for recycling

- disposal costs

- must not reduce the quality of the product required or affect the intended use of the product

- must not significantly impact the acquisition cost

    - Are the quoted price(s) on this tender (where applicable) available to our employees?

Yes	      	No 	       N/A

Administratively the Western Integrated Health Authority will not be involved in ordering, servicing, warranty and payment; the employee(s) would deal directly with the company.

1.6	Tender Acceptance

1.6.1	Any acquisitions resultant from this invitation to Tender shall be subject to the Public Tendering Act.

    - The Tenders shall be opened in the Private Dining Room at The Western Memorial Regional Hospital on the scheduled date and time.

    - Any Tender may be accepted in whole or in part.  The lowest Tender may not necessarily be accepted and Western Health reserves the right to cancel the Tender call.  Western Health shall not be held responsible or liable for the payment of any costs that are incurred by the bidder in preparing a Tender in response to this invitation to Tender.

1.7	Warranty

The Vendor shall warrant that the product supplied to Western Health shall equal or exceed the published specifications.  Must have a minimum  1 year on parts and service and 5 year warranty on parts.  Please provide warranty information with your bid.

- Product Specifications

The dishwasher is to be a replacement for Hobart Model AM14P.  The replacement is is required to be a corner unit that will tie into existing soiled and clean dish table feeds, existing plumbing with none or  very minimal modifications needed.  Space in the area is limited and height of the replacement machine must not exceed that of current machine.  Potential bidders can visit  the site to ensure the measurements of the unit they are proposing fits properly.  Bidders may chose not to visit the site  however they must guarantee the unit they bit  will fit properly into the allotted space.

The dishwasher mus also t meet the following specifications:

-A Door-Style Tall Dishwasher with electric tank heat and built-in 8.5 KW Hot Water booster heater that is rated for 5o+ Racks per Hour and provide Hot Water Sanitizing.

-Electrical Requirements include:   208/60/3 with two connections.  One 30 amp connection for tank heat, motor & controls and one 30 amp connection for 8.5 KW booster heater.

-	The unit must be NSF certified to clean pots, pans and other dishware within timed wash cycles (range 1, 2, 4, & 6 min cycles).

-	Must have a 27” door opening to allow for 18” x 26” sheet pans.

-	Must have Solid state, integrated controls with digital status indicators.

-	Must have Two (2) HP.(1.5 kw) Self draining pump and impeller.

-	Must be Self-draining, high efficiency stainless steel pump and stainless steel impeller.

-	Must be Stainless steel construction:  drawn tank, tank shelf, chamber, trim panels, frame and feet.

-	Must have a system for separating debris from water -  scrap screen and basket 	system.

-	Must have Automatic Fill and automatic drain closure.

-	Must have Vent fan control.

-	Must have De-liming cycle.

-	Must have Service diagnostics.

-	Must have Electric Booster Heater of 70º F (21º C) rise & interconnected booster heater control

-	Must have Splash panel kit for Corner Installation

-	Must have Pressure regulator valve, ¾”, with internal thermal expansion bypass.

Ergonomic/safety considerations:

-	Must have spring counterbalanced chamber with polyethylene guides so door is easy to lift.

-	Must have revolving, interchangeable upper and lower anti-clogging wash & rinse arms

-	Must have Door actuated start.

-          The successful vendor will be required to provide on-site training to staff in the  care and use of the dishwasher as well as routine maintenance and cleaning procedures.

Bidders must provide full details of the make and model of any unit being proposed.

Recommended:

*  On site visit required by supplier representative to be sure dishwasher meets specifications and  requirements for installation at site.

*  Service; Manufacturer required to identify local factory trained technicians available for service requirement during and after warranty period.  Full service contracts to be available after warranty period.

3.0	Presentation / Training / Service

  - Presentation

A presentation of the Tender and / or a demonstration of the product / system shall be provided, if requested, at the Vendor’s expense.

- Financial Considerations

  - All applicable taxes shall be indicated in the Tender.

  - Terms of Payment

The Authority agrees to pay the full invoiced amount within 30 days following acceptance of the installed system by Western Health.  Acceptance testing will be completed within 30 days following the complete installation of the system.

- Vendor Confirmation (please sign)

I confirm that our Tender meets or exceeds the specifications detailed in this invitation to Tender.  I also confirm that all specifications are included in the quoted price.  Any items that are optional are noted accordingly.

Signed

Title

Company Name

Address                    _________________________

_________________________

Phone                       _________________________

- Bid Price for supply of Dishwasher delivered to site :  ___________________

- Bid price for installation:   _______________________

Tax Extra  	Yes _____ No _____

## TENDER CHECKLIST

TENDER #0271-1626

DID YOU INCLUDE

HAS TENDER SUBMISSION BEEN SIGNED					Yes 	    No

COPY OF REQUIRED TENDER DOCUMENTS    				Yes 	    No

COPY OF BROCHURES (IF REQUESTED)					Yes 	    No

COPY OF WCB LETTER OF GOOD STANDING (IF REQUIRED)		Yes 	    No

COPY OF PROOF OF INSURANCE (IF REQUIRED)				Yes 	    No

AMOUNT OF TAX NOTED ON REQUEST FOR QUOTATION FORM	Yes 	    No

OPTIONAL PRICING FOR TRAINING INCLUDED				Yes 	    No

NOTE:  	TENDER RESPONSES MAY BE REJECTED IF YOU ANSWER “NO” TO ANY OF THE ABOVE QUESTIONS.